IOP-SANFO-581312006

5GHz 13.5dBi Sector Antenna

| Electrical Specification |
| --- |
| Frequency range | 4900 – 5150MHz | 5150 – 5875MHz |
| Gain | 12.5 dBi | 13.5 dBi |
| VSWR | 2 : 1 Max. | 2 : 1 Max. |
| Polarization | Linear, Vertical | Linear, Vertical |
| HPBW / Horizontal | 120° | 120° |
| HPBW / Vertical | 6° | 6° |
| Electrical downtilt | 0° | 0° |
| Power handing | 5W (cw) | 5W (cw) |
| Impedance | 50 Ohms | 50 Ohms |
| Connector | N Jack | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Lightning protection | DC ground |
| Radome color | Gary - white |
| Radome material | ABS,UV resistant |
| Weight | 555g |
| Dimensions | 620 × 88 × 70 mm |