IOP-PANFO-DT1404441

2.4 & 5GHz 11 & 14dBi Dual Band Three Polarization Panel Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400 – 2500MHz | 5150 – 5875MHz |
| Gain | 11 dBi | 12 ~ 14 dBi |
| VSWR | 2 : 1 Max. | 2 : 1 Max. |
| Polarization | Linear, Vertical & Horizontal | Linear, Vertical & +- 45° |
| HPBW / Horizontal | 40 - 44° | 19 - 22° |
| HPBW / Vertical | 38 - 41° | 25 - 31° |
| Sidelobes level | -10dB (Max) | -8dB (Max) |
| Front to back ratio | -20dB (Max) | -20dB (Max) |
| Isolation | -15dB (Min) | -22dB (Min) |
| Power handing | 10W (cw) | 6W (cw) |
| Impedance | 50 Ohms | 50 Ohms |
| Connector | N Jack × 3 |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +70℃ |
| Humidity | 95% @ 55℃ |
| Lightning protection | DC ground |
| Radome color | White |
| Radome material | ABS, UV resistant |
| Weight | 1720g |
| Dimensions | 360 × 360 × 16 mm |
| Waterproof | IP-X7 |
| Mounting kit | Pole mount & Wall mount |