IOP-OANMO-DB0536030

2.4 & 5GHz 2.5 & 5dBi Dual Band Omni Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400 – 2483MHz | 5150 – 5875MHz |
| Peak gain | 4.5 dBi | 7.0 dBi |
| Average gain | 2.5 dBi | 5.0 dBi |
| VSWR | 2 : 1 Max. | 2 : 1 Max. |
| Polarization | Linear, Vertical | Linear, Vertical |
| HPBW / Horizontal | 360° | 360° |
| HPBW / Vertical | 30° | 15° |
| Power handing | 2W (cw) | 2W (cw) |
| Impedance | 50 Ohms | 50 Ohms |
| Connector | N Plug | N Plug |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +70℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gray |
| Radome material | ABS |
| Weight | 70g |
| Dimensions | Φ22 × 183 mm |