IOP-MANFO-241436030

2.4GHz 14dBi Mobile Car Dome Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400MHz – 2500MHz |
| Gain | 4 dBi / 14dBi (with Booster) |
| VSWR | 2 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 360° |
| HPBW / Vertical | 30° |
| Power handing | 5W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Booster Electrical Specification |
| Frequency range | 2400MHz – 2500MHz |
| Output Power @ 1dB Compression | 30dBm (Typ.) |
| Linear Output Power | 27-30dBm @ 802.11b / 11Mbps |
|  | 23-26dBm @ 802.11g / 54Mbps |
| EVM at Pout = 24dBm | 5.6% |
| Tx Mode Turn on Power | -1 dBm (Min.) |
| Fixed Transmit Gain | 10 dB (Typ.) |
| Receiver Input Power | -15 dBm (Max.) |
| Receiver Gain | 10 dB (Typ.) |
| Noise Figure | 3.7 dB |
| Input / Output VSWR | 2 (Max.) |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -20℃ to +70℃ |
| Humidity | 95% @ 55℃ |
| Waterproof | IP-X7 |
| Lightning protection | DC ground |
| Radome color | White |
| Radome material | PC |
| Weight | 980g |
| Dimensions | 200 x 118 x 90 mm |